## Slide 1
TURBOMACHINERY DESIGN SOFTWARE
Multi-Fidelity Design of
3D Turbo Centrifugal Fan
By Using iDesignFan Turbo Design Module V4.1
㈜에어로네트 · 인하대학교 유동소음제어연구실
August 20, 2026

## Slide 2
Turbo Centrifugal Fan Market
Most widely used fluid machines in HVAC, industrial
ventilation, and process cooling, especially Data Ceneter
Cooling Module, contributing to significant share of global
electricity consumption (1.5 ~ 2.5%), Even 1 % increase of
efficiency yielding huge energy savings ( 6,600 ~ 11,000
Gwh).
Conventional Design Optimization by high-fidelity CFD
Huge amount of computational resources for high-
dimensional design space cases.
Machine-learning Surrogate Models
Quick response by CFD of negligible cost, Enabling
broader and faster exploration in multi-design spaces.
<Cooling for Data Center>
<Cooling for Fuel Cell>
Multi-Fidelity Design of 3D Turbo Centrifugal Fan
Introduction
02 / 19

## Slide 3
TE
LE
Conventional Design
3D Sweep Control
-10° (CW)
+3°
-6.9° (CW)
-Ω (CW)
(CCW)
Software Design Methods & Procedures
3D Design by Blade Control
03 / 19

## Slide 4
#1
#2
#3
#51
#52
#53
#98
#99
#100
Design Parameters | Value
Diameter (D) | 630 mm
Rotation Speed (N) | 1000 rpm
Blade Thickness | 4 mm
Flow Rate (Q) | 2 m3/s
Outlet Width (b2) | 230 mm
Design Example
Software Design Methods & Procedures
Latin Hypercube Sampling (LHS)
04 / 19

## Slide 5
Low-fidelity CFD Domain
High-fidelity CFD Domain
3D
2D
5D
Perfromance Chamber Analogy
Software Design Methods & Procedures
CFD Domain Example
05 / 19

## Slide 6
GPR surrogate model accuracy
Global Exploring for
High Efficiency
Local Exploring for
High Efficiency
Multi-Fidelity Design of 3D Turbo Centrifugal Fan
Optimization Method by Machine Learning
06 / 19

## Slide 7
Vorticity Isosurfaces
of LHS Fans
) +GB(
L.F. Model Sound
Computation Example (LF#4)
Vorticity Contour (LF #4 )
Multi-Fidelity Design of 3D Turbo Centrifugal Fan
Low-fidelity Optimization Fan Geometry
07 / 19

## Slide 8
iDesignFan Turbo Centrifugal Module
Step 1 – Design Goal
08 / 19

## Slide 9
iDesignFan Turbo Centrifugal Module
Step 2 – Airfoil Design Parameter Input
09 / 19

## Slide 10
iDesignFan Turbo Centrifugal Module
Step 2 – Blade Bezier Curve Design
10 / 19

## Slide 11
Backplate
Shroud
Chart: ß2b [ ° ]
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
0.98 | 19.345 | 16.9456 | 15.037 | 13.4853 | 12.1976 | 11.1086 | 10.1716 | 9.3516 | 8.6217 | 7.9587 | 7.3268
1 | 17.1526 | 15.5848 | 14.2455 | 13.087 | 12.0726 | 11.1742 | 10.3693 | 9.6398 | 8.9702 | 8.3448 | 7.7324
1.1 | 11.7297 | 11.546 | 11.3911 | 11.2656 | 11.1708 | 11.1083 | 11.0806 | 11.0905 | 11.1411 | 11.2339 | 11.3459
Backplate
Shroud
Pressure Factor 값에
따른 날개 출구 각 계산 예
iDesignFan Turbo Centrifugal Module
Step 2 – Total Pressure Distribution Input
11 / 19

## Slide 12
< XY View of Aligned Airfoils >
< YZ View of Aligned Airfoils >
iDesignFan Turbo Centrifugal Module
Step 3 – Airfoil Parameter Input
12 / 19

## Slide 13
< 3D Design Example >
Sweep 적용
iDesignFan Turbo Centrifugal Module
Step 4 – 3D Review and Control
13 / 19

## Slide 14
iDesignFan Turbo Centrifugal Module
Step 5 – 3D Modeling (e.g. SolidWorks)
14 / 19

## Slide 15
iDesignFan Turbo Centrifugal Module
Step 5 – 3D Modeling (e.g. NX)
15 / 19

## Slide 16
iDesignFan Turbo Centrifugal Module
Step 5 – TurboGrid, CFX Domain Export
16 / 19

## Slide 17
Model # | Fan Config. | Blade | L.E Curvature Coeff. | Camber Angle [°] | Hub_Sweep [°] | Mid_Sweep [°] | Shroud_Sweep [°] | η_Fan (%) | Γ (m2/s)
LF #4 |  | 7 | 0.4 | 0 | -13.64 | -1.94 | -1.35 | 69.99 | 122.16
M.L #1 |  | 6 | 0.054 | -0.86 | -4.99 | 6.11 | 12.72 | 70.04 | 106.13
M.L #2 |  | 6 | -0.087 | -1.8 | -3.14 | 6.02 | 12.60 | 70.23 | 97.52
M.L #3 |  | 7 | 0.28 | 0.19 | -13.37 | 1.09 | 3.36 | 71.04 | 97.35
High-fidelity Optimization Fan Geometry
High-fidelity Simulation Model Examples
17 / 19

## Slide 18
Q-criterion (value : 200,000 [s-2 ])
Outlet
Total Pressure
Distribution
TE
LE
< M.L #2>
< LHS #10, η : 64.62 %,
Γ : 123.56 m2/s >
LE
TE
Inlet
10,000,000 cells, y+ ≈ 1
Turbulent Model
Stress-Blended Eddy Simulation (SBES)
High-fidelity CFD (ANSYS CFX)
3D CFD Meshing and Result Example
18 / 19

## Slide 19
Verification Result of M.F. Design Using iDesignFan Software
Best Optimal Design (M.L #3) of ηs = 71.04%, +1.05 % over Manufactured Model (66.5%),
with 20% Lower Circulation Strength (Γ: 122.16 → 97.35 m²/s) compared with Low-fidelity Outcome.
Efficiency Gain and Reduced Noise with Reduced Circulation
Same Loading with Increased Vortex Strength Index Criterion, Meaning that Excess Vortex
Circulation Resulting in Losses in Backward-swept Impellers.
Global Search of Priori-favoring Moderate-Γ designs over High-Γ Ones
Local GPR Refinement Accelerating the Trend faster.
Very-Efficient, AI M.L. Fan Design Software
Multi-Fidelity Design of 3D Turbo Centrifugal Fan
Conclusions
19 / 19